## Slide 1
CHƯƠNG 2 : GIAO THỨC ĐỊNH TUYẾN EIGRB - PART1
Configure
Neighbor
Metric
Load Balancing

## Slide 2
EIGRP: Administrative Distance
OSPF
10.0.0.0/8
OSPF
AD 110
EIGRP
100M
200ms
50% 50M/100M
100% packet
Bandwidth
Delay
Load
Reliability
EIGRP
AD 90
R1
R2
R3
R1# show interface f0/2

## Slide 3
EIGRP: AS (Autonomous System)
R1
R2
172.16.1.1/24
.1
.2
172.16.3.1/24
R1(config)# router eigrp 100
R1(config-router)# network 172.16.0.0 0.0.255.255
R1(config-router)# network 172.16.1.0 0.0.0.255
R1(config-router)# network 172.16.2.0 0.0.0.255
R1(config-router)# network 172.16.3.0 0.0.0.255
172.16.2.1/24
192.168.12.0/24
interface f0/0
ip router eigrp 100
f0/0
R1# show ip eigrp interface brief
IP Preference vs Wildcard Mask

## Slide 4
EIGRP: AS (Autonomous System)
R1
R2
172.16.1.1/24
.1
.2
172.16.3.1/24
R1(config)# router eigrp 100
R1(config-router)# network 172.16.0.0 0.0.255.255
R1(config-router)# network 172.16.1.1 0.0.0.0
R1(config-router)# network 172.16.2.1 0.0.0.0
R1(config-router)# network 172.16.3.1 0.0.0.0
172.16.2.1/24
192.168.12.0/24
interface f0/0
ip router eigrp 100
f0/0
R1# show ip eigrp interface brief
IP Preference vs Wildcard Mask

## Slide 5
EIGRP: Major Network
Major Network | Subnet
10.0.0.0/8 | 10.0.0.0/24
172.16.0.0/16 | 172.16.0.0/24
192.168.1.0/24 | 192.168.1.0/30

## Slide 6
EIGRP: auto-summary
10.0.0.1
10.0.0.2
192.168.1.64/26
172.16.1.64/26
10.0.1.64/26
192.168.1.0 /26
R1(config)# router eigrp 100
R1(config-router)# network 0.0.0.0 255.255.255.255
R1(config-router)# no auto-summary
R1
R2

## Slide 7
EIGRP: auto-summary
R1(config)# router eigrp 100
R1(config-router)# network 0.0.0.0 255.255.255.255
R1(config-router)# no auto-summary
192.168.1.0/24
10.0.0.1
10.0.0.2
192.168.1.64/26
172.16.0.0/16
172.16.1.64/26
10.0.0.0/8
10.0.1.64/26
192.168.1.0 /26
R1
R2

## Slide 8
EIGRP: default-route
ip route 0.0.0.0 0.0.0.0 ISP
router eigrp 100
redistribute static
10.0.0.1
10.0.0.2
R1# show ip route eigrp
D*EX 0.0.0.0/0 [170/28160] via 10.0.0.2, 00:00:11, FastEthernet0/0
ISP
EIGRP 100
R2
R1

## Slide 9: EIGRP Neighbor
ip hello-interval eigrp 5
ip hold-time eigrp 15
224.0.0.10
10.0.0.1
hello: 5s
1. Autonomous System
2. Subnet
3. Authentication
4. K value
5. MTU
router eigrp 100
router eigrp 100
AS
AS
MTU
1504
MTU 1500

## Slide 10
EIGRP: Neighbor Condition
Autonomous System
Subnet
Authentication
K value
MTU
Stub area flag
10.0.0.1
10.0.0.2
/24
/24
MTU
1500
MTU
9000
172.16.0.0/16
R# show ip eigrp neighbor detail
Address Interface Holdtime Uptime Q Seq SRTT RTO
(secs) (h:m:s) Count Num (ms) (ms)
10.0.0.2 f0/1 13 0:00:41 0 11 4 20
Optical
Converter
224.0.0.10
hello: 5s
router eigrp 100
router eigrp 100
AS
AS
ip hello-interval eigrp 5
ip hold-time eigrp 15

## Slide 11: Auto Summary
172.16.1.0/24
172.16.1.0/24
172.16.2.0/24
DS1
DS2
172.16.3.0/24
192.168.1.0
172.16.0.0/16

## Slide 12
EIGRP: Neighbor Condition

## Slide 13
R# clear ip eigrp neighbors 10.0.12.1
R# clear ip eigrp neighbors f0/1
10.0.234.3
10.0.234.4
10.0.12.1
f0/1
f0/0
R# show ip eigrp interfaces
IP EIGRP interfaces for process 77
Xmit Queue Mean Pacing Time Multicast Pending
Interface Peers Un/Reliable SRTT Un/Reliable Flow Timer Routes
f0/1 1 0/0 0 11/434 0 0
f0/0 2 0/0 337 0/10 0 0
Notes: Purpose: This figure presents the IGRP metric with its five possible components.
Emphasize : Bandwidth and delay are the two metrics that are most commonly used. They also comprise the default metric.
Note: Changing IGRP metrics can have great impact on network performance.
Describe the IGRP 24-bit metric field, as follows:
  Bandwidth—Minimum bandwidth on the route, in kilobits per second.
  Delay—Route delay, in tens of microseconds.
  Reliability—Likelihood of successful packet transmission, expressed as an integer from 0 to 255.
  Loading—Effective bandwidth of path.
  MTU—Minimum MTU in path, expressed in bytes.
The following equation calculates the metric. It is presented for instructors and is not required to be taught:
  metric = [k1 x bandwidth + (k2 x bandwidth) / (256 - load) + k3 x delay]
If k5 does not equal 0, an additional operation is done:
  metric = metric x (k5/(reliability + k4))
The default constant values are k1 = k3 = 1 and k2 = k4 = k5 = 0.
Again, if default values are set, metric = bandwidth + delay.
The constants (k1, k2, k3) can be changed using the metric weights command. Changes to the IGRP constant values should be made with great care.

## Slide 14
EIGRP: Metric
Default | K1 | K2 | K3 | K4 | K5
 | 1 | 0 | 1 | 0 | 0
tos | BW | Load | Delay | Reliability | 
R(config)#
metric-weight 0 1 0 1 0 0
Metric =

## Slide 15
EIGRP: Metric
BW 8000 M
Dl 5000 us
BW 1,5 M
Dl 20000 us
BW 100 M
Dl 100 us
R1
R2
R3
Metric =
Metric =
R3(config-if)# bandwidth 100000 (kbps)
R3(config-if)# delay 10 (ten of microsecond)
3.3.3.3/24
R1# show ip route eigrp
D 3.3.3.0 [90/2300416] via 10.0.12.2, 00:13:22, FastEthernet0/0
R3# show interface f0/0 | include .*BW.*DLY
MTU 1500 bytes, BW 8000000 Kbit/sec, DLY 5000 usec,

## Slide 16
EIGRP: Metric
R1# show ip eigrp topology 3.3.3.0/24
IP-EIGRP (AS 99): Topology entry for 3.3.3.0/24
State is Passive, Query origin flag is 1, 1 Successor(s), FD is 2300416
Routing Descriptor Blocks:
10.0.12.2 (FastEthernet0/0), from 10.0.12.2, Send flag is 0x0
Composite metric is (2300416/2297856), Route is Internal
Vector metric:
Minimum bandwidth is 1544 Kbit
Total delay is 25100 microseconds
Reliability is 255/255
Load is 1/255
Minimum MTU is 1500
Hop count is 2
R1#

## Slide 17
EIGRP: Feasible Distance vs Advertise Distance
Net A
R1
R3
R5
AD = 1100
Network | Next-hop | FD | AD
A | R3 | 2000 | 1100
FD = 2000

## Slide 18
EIGRP: Load Balancing
40
RouterE# show ip route
D 172.16.0.0 [90/409600] via RouterC, F0/2
Feasible Successor
Successor
RouterE# show ip route
D 172.16.0.0 [90/409600] via RouterC, F0/2
D 172.16.0.0 [90/409600] via RouterB, F0/1
Dual

## Slide 19
50
Net A
R1
R2
R3
R5
900
1100
100
Network | Next-hop | FD | AD
A | R2 | 1000 | 900
A | R3 | 1150 | 1100
A | R4 | 3000 | 800
Successor
Feasible Successor
1050
1100
FD cung cấp đường dự phòng, đảm bảo mạng hội tụ nhanh, chống loop
Notes: Purpose: This figure presents the IGRP metric with its five possible components.
Emphasize : Bandwidth and delay are the two metrics that are most commonly used. They also comprise the default metric.
Note: Changing IGRP metrics can have great impact on network performance.
Describe the IGRP 24-bit metric field, as follows:
  Bandwidth—Minimum bandwidth on the route, in kilobits per second.
  Delay—Route delay, in tens of microseconds.
  Reliability—Likelihood of successful packet transmission, expressed as an integer from 0 to 255.
  Loading—Effective bandwidth of path.
  MTU—Minimum MTU in path, expressed in bytes.
The following equation calculates the metric. It is presented for instructors and is not required to be taught:
  metric = [k1 x bandwidth + (k2 x bandwidth) / (256 - load) + k3 x delay]
If k5 does not equal 0, an additional operation is done:
  metric = metric x (k5/(reliability + k4))
The default constant values are k1 = k3 = 1 and k2 = k4 = k5 = 0.
Again, if default values are set, metric = bandwidth + delay.
The constants (k1, k2, k3) can be changed using the metric weights command. Changes to the IGRP constant values should be made with great care.

## Slide 20
Net A
R1
R2
R3
R4
S
F.S

## Slide 21
Net A
R1
R2
R3
R4
Network | Next-hop | FD | AD
A | R4 | 20 | 10
A | R1 | 50 | 40
10
10
10
10
10
Successor

## Slide 22
EIGRP: Topology Table
R# show ip eigrp topology all-link
…
P 172.16.0.0 255.255.0.0, 2 successors, FD is 4200700
via 192.168.1.2 (4200700/800200), Ethernet0
via 192.168.2.2 (4200700/600200), Ethernet1
via 192.168.3.2 (4600900/600200), Serial0
via 192.168.4.2 (5600300/4800700), Serial1
FD
AD

## Slide 23
EIGRP: Topology Table
Router# show ip route 172.16.0.0
Routing entry for 172.16.0.0/16
Known via “eigrp 100″, distance 90, metric 300200, type internal
Redistributing via eigrp 100
Routing Descriptor Blocks:
* 192.168.1.2, from 192.168.1.2, 00:00:56 ago, via Serial0/1
Route metric is 300200, traffic share count is 3
Total delay is 40100 microseconds, minimum bandwidth is 1280 Kbit
Reliability 255/255, minimum MTU 1500 bytes
Loading 1/255, Hops 2
192.168.2.2, from 192.168.2.2, 00:00:56 ago, via Serial0/0
Route metric is 900600, traffic share count is 1
Total delay is 20100 microseconds, minimum bandwidth is 256 Kbit
Reliability 255/255, minimum MTU 1500 bytes
Loading 1/255, Hops 1

## Slide 24: EIGRP Load Balancing
R0
R2
R1
R3
path 1: 1100
path 2: 1100
path 3: 2000
path 4: 4000
R4
172.16.0.0/16
the traffic share count for
path 1: 4000 / 1100 = 3 packet
path 2: 4000 / 1100 = 3 packet
path 3: 4000 / 2000 = 2 packet
path 4: 4000 / 4000 = 1 packet
RouterX(config-router)# maximum-paths [1-16] “default 4

## Slide 25: Configuring a Floating Static Route