## Slide 1: Outcome 2: Inspection
Perform a visual inspection on a low voltage electrical installation

## Slide 2: Visual Inspection
Inspection Checklist
Full list of inspections can be found in IET wiring Regulations BS7671
Labels on equipment/cables with reference to layout diagrams
Bonding/Earthing
Cable/conductor sizes
Cable types
Connections/terminations
BS/CE symbols
Damaged equipment
Rating of equipment
Suitability of accessories
Positioning of Equipment

## Slide 3: Labelling
Throughout your inspection you need to lookout for correct labelling. For example- consumer unit should contain details of when it was last inspected , with the date initials and the company which carried out the test.

## Slide 4: Bonding/Earthing
The purpose of earth bonding in electrical systems is to protect people and equipment from current leakage which can cause injury or damage to equipment or material.
Without earthing, an electrical fault in your home could mean you would get a severe electric shock. Earthing prevents this by providing a way for an electrical current to flow back to the fuse board and not though you.
Earthing Typically carried out with the copper pipes in the house.

## Slide 5: Cable Type and Size
Cable sizes must be the correct size as this determines the amount of current, they can carry. The wrong size can lead to damage of cables. The type of cable used it also important; it must suit the environment the cable is in. Such as heat proof , armour etc.
During your inspection look out of any signs of overheating. If possible, try to ensure the correct cable size is used. This can be checked from a consumer unit. In a typical house a 1.5mm cable is used for lighting and 2.5mm for sockets. However, it all depends on the load they are carry. An electric shower or cooker will have a larger cable. 6mm-10mm.

## Slide 6: Cable Terminations
Poor cable terminations can lead of fires- During your inspection again look out for any signs off hot spot or over heating especially on sockets and breakers.

## Slide 7: Positions and Maintenance
The equipment should be mounted so that it is safe and we have access for maintenance. Also we must check to see if spare part are available and its not become obsolete.

## Slide 8: Rating Of Equipment's
Every electrical equipment's has a rating. This is usually given in power (Watts) . We also ensure that the equipment is certified for its intended use. Some equipment also has the efficiency rating.

## Slide 10: Example Checklist